## Slide 1: SADRC Presentation Feb 17th, 2024 Presented by Doug - N8IQT

## Slide 2: Agenda
Overview of Wires X and YSF. We will not focus on any other digital modes in this presentation.
Wires X
YSF
Bridging YSF to Wires X
Shark Open, Spot, Pi-Star, and Digital Thumb DV
Yaesu capable equipment
Yaesu Digital Repeater and Wires X Box (HRI-200)

## Slide 3: What is Wires-X
Wires X – (Wide-coverage Internet Repeater Enhancement System) is an Internet communication system which expands the range of repeaters and nodes.
WIRES-X Node - An amateur “Node” station is where you use of one of Yaesu’s C4FM Fusion model radios connected to the internet using Yaesu’s software to link world-wide.
Amateur stations can communicate with other amateur stations using a node radio either on RF simplex or direct using a microphone. This is referred to as a PDN. (see next bullet below)
PDN – Personal Digital Node – Capable of using your own C4FM Fusion radio to connect to Wires X without going through a repeater.
A Wires X box (HRI-200) is only required when operating a room capable of having multiple connections generally used for repeater applications requiring several inbound connections.

## Slide 4: YSF (Independent Network)
YSF - Short for Yaesu Fusion. It is an open-sourced software and managed by amateurs who update the code from time to time. It is not a Yaesu or Wires X product as many people believe.
Unlike Yaesu Wires X, there is no central management server or management of rooms. There are directories of YSF Servers.
YSF CAN NOT directly connect to Wires X on a Yaesu
Fusion repeater network without a bridge!
In order to connect a YSF server to Wires X, SADRC bridges the 2 connections using a Shark Open Spot.

## Slide 5: What is Bridging?
A bridge is a way of connecting 2 different protocols or technologies together.
Since YSF can’t directly talk to Wires X, a bridge is required so that signals can be heard on both YSF and Wires X.
When a signal is heard on YSF server, an Open Spot or PI-Star unit is located at the repeater site and transmits to the Yeasu repeater. When it hears a signal on YSF it transmits out on Wires X (bridging the 2 protocols together).

## Slide 6: Ways to Connect to SADRC!
VHF & UHF Repeaters linked to Texas SADRC
Wires X Software and PDN Node – Texas SADRC Room #40324
YSF Network – US SADRC (Reflector #84398) using an RF Shark or Pi-Star
Digital Thumb DV - No transceiver required. Operates off your computer and external microphone.

## Slide 7: RF Shark OpenSpot

## Slide 8: Pi-Star Hot Spots

## Slide 9: DB3000U Digital Thumb DV
Thumb DV
nwdigital@radio.com
No transceiver required. Need computer and external Microphone.

## Slide 10: YSF & Wires X Dashboards
YSF Reflector Dashboard
https://www.pistar.uk/ysf_reflectors.php
Wires X Active Nodes
WIRES-X ACTIVE NODE ID list (yaesu.com)
Will conduct a live demonstration of Wires X and YSF at end of this presentation.

## Slide 11: Yaesu C4FM Current 2024 Models
FT991A
FTM-200DR
FTM-300DR
FTM-500DR
FT-70DR
FT-5DR

## Slide 12: System Fusion Repeater and HRI-200
DR2X State of Art C4FM Repeater
HRI-200
HRI
**You do NOT require the Wires HRI-200 to connect to a Wires X room. You simply connect your HT or mobile radio to a PC and download the Wires X software. You will need to obtain a Wires X ID from Yaesu in order to operate. This is known as a PDN (Personal Digital Node). The HRI-200 is required to have multiple connections such as Texas SADRC #40324 with 20-30 repeaters connected.

## Slide 13: Texas SADRC Wires X Room Repeaters What is a Wires X Room?

## Slide 14: SADRC Network
YSF Server and Software Upgrade
SADRC Repeater Network Linked to SADRC
Clubs and Independent Repeaters
Select Heat Maps (coverage maps)
New Repeater Site Opportunities
Live Demonstration
Q&A – Wrap up!

## Slide 15: YSF Server and Software Upgrade
Current YSF server is being decommissioned and we will be upgrading to a new server and updated YSF software.
Team was set up to review all server options and costs.
Stability of the network connection and software are key!
K9EQ of the MNW group has written new code to provide us with the most stable operating software.
Plan is to use a high-speed server with redundancy out of NY. Chris K9EQ will manage the software, upgrades, as well as the server
A dashboard will be available to allow our group to view who’s connected on YSF

## Slide 16: SADRC Repeater Network Wires X 40324, YSF US SADRC

## Slide 17: Other Club Partners
Clubs or Independent Repeaters linked to Texas SADRC
  Kendall Amateur Radio Club (KARS) Boerne, TX
  444.900 & 444.925
  MCARC – Hondo – 443.350
  KA5C – University of Texas – Austin - 442.150
  NU5DE – McDade 441.575
  K7RHT – Kerrville – 147.040 (New)
  K5ENT – Corpus Christi – 442.575

## Slide 18: New - 443.200 - SW San Antonio - WS5DRC

## Slide 19: 147.160 N. Bexar County – N8IQT

## Slide 20: 442.750 N. Bexar County – N8IQT

## Slide 21: 440.275 Blanco/Comal – WS5DRC 281 at 306

## Slide 22: 147.160 Round Rock – K5UUT

## Slide 23: 147.040 Kerrville - K7RHT

## Slide 24: 442.575 Corpus Christi – K5ENT

## Slide 25: New Repeater Site Opportunities
Llano, TX – SADRC - 147.220 – Planning in 2024
Corpus Christi – STARC Club. 146.880 – 600 Foot tower. Exploratory discussions.
San Angelo, TX – WM5L - 444.525 PL 162.2 AMS mode. Connecting to SADRC – April 2024
I35 Project - NE San Antonio – TBD
N. Loop1604/281 Project –TBD – Possibility

## Slide 26: SADRC - 147.220 Llano – 2024 Project 300 Foot TV Tower

## Slide 27: 147.220 Llano &147.160 Round Rock

## Slide 28: N. Loop 1604/281 Opportunity

## Slide 29: Live Demonstration
Wires X – Live Demonstration and dashboard view.
YSF – Live demonstration and dashboard view.
Visual understanding of how we bridge these two modes on SADRC.

## Slide 30: up. 0
Q&A
Wrap up